Computational Methods Chapter 4
Solving Systems of Linear Equations

4.1 Background

1. Many engineering problems can be posed as solving systems of linear equations:
  1. Trusses (Newton's Laws)
  2. Circuits (Kirchoff's Law)
  3. Motion of objects with internal connections and linkages (ordinary differential equations)
  4. Stress/strain/deformation (partial differential equations)
  5. Fluid Motion (partial differential equations)
  6. etc…
2. Cramer's Rule – directly solve for 3x3 (but not bigger)
left[ {matrix{a_11 # a_12 # a_13 ## a_21 # a_22 # a_23 ## a_31 # a_32 # a_33} }right] left[ {matrix{ x_1 ## x_2 ## x_3 } } right] = left[ {matrix{ b_1 ## b_2 ##b_3 } } right]

x_1 = {left lline {matrix{b_1 # a_12 # a_13 ## b_2 # a_22 # a_23 ## b_3 # a_32 # a_33} } right rline } over {left lline {matrix{a_11 # a_12 # a_13 ## a_21 # a_22 # a_23 ## a_31 # a_32 # a_33} } right rline }	x_2 = {left lline {matrix{a_11 # b_1 # a_13 ## a_21 # b_2 # a_23 ## a_31 # b_3 # a_33} } right rline } over {left lline {matrix{a_11 # a_12 # a_13 ## a_21 # a_22 # a_23 ## a_31 # a_32 # a_33} } right rline }	x_3 = {left lline {matrix{a_11 # a_12 # b_1 ## a_21 # a_22 # b_2 ## a_31 # a_32 # b_3} } right rline } over {left lline {matrix{a_11 # a_12 # a_13 ## a_21 # a_22 # a_23 ## a_31 # a_32 # a_33} } right rline }

1. “Clever” substituting (2x2, 3x3… not bigger)
2. Direct and Iterative Methods
In general we are trying to solve:

left[ {matrix{a_11 # a_12 # a_13 #a_14 ## a_21 # a_22 # a_23# a_24 ## a_31 # a_32 # a_33# a_34 ## a_41 # a_42 #a_43 #a_44} }right] left[ {matrix{ x_1 ## x_2 ## x_3 ## x_4 } } right] = left[ {matrix{ b_1 ## b_2 ##b_3 ##b_4} } right]

1. Upper Triangular Form
  1. left[ {matrix{a_11 # a_12 # a_13 #a_14 ## 0 # a_22 # a_23# a_24 ## 0 # 0# a_33# a_34 ## 0 #0 #0 #a_44} }right] left[ {matrix{ x_1 ## x_2 ## x_3 ## x_4 } } right] = left[ {matrix{ b_1 ## b_2 ##b_3 ##b_4} } right]
  2. Which can be solved by:
  3. x_4 = b_4 over a_44 newline x_3 = { b_3 - a_34 x_4 } over {a_33} newline x_i = { b_i - sum from{j=i+1} to{j=n} a_ij x_j } over { a_ii} ~~~~~~ i=n-1,`n-2,`...,`1
  4. This is called backsubstitution
2. Lower Triangular Form
  1. left[ {matrix{a_11 # 0 # 0 #0 ## a_21 # a_22 # 0# 0 ## a_31 # a_32# a_33# 0 ## a_41 #a_42 #a_43 #a_44} }right] left[ {matrix{ x_1 ## x_2 ## x_3 ## x_4 } } right] = left[ {matrix{ b_1 ## b_2 ##b_3 ##b_4} } right]
  2. Which can be solved by:
  3. x_1 = b_1 over a_11 newline x_2 = { b_2 - a_21 x_1 } over {a_22} newline x_i = { b_i - sum from{j=1} to{j=i-1} a_ij x_j } over { a_ii} ~~~~~~ i=2,`3,`...,`n
  4. This is forward substitution.
3. Diagonal Form
  1. left[ {matrix{a_11 # 0 # 0 #0 ## 0 # a_22 # 0# 0 ## 0 # 0# a_33# 0 ## 0 #0 #0 #a_44} }right] left[ {matrix{ x_1 ## x_2 ## x_3 ## x_4 } } right] = left[ {matrix{ b_1 ## b_2 ##b_3 ##b_4} } right]
  2. Which can be solved by:
  3. x_i = b_i over a_ii
4. As you might guess… the problems are very seldom like above… BUT we can make them look this way!

Developing an algorithm for back substitution (this assumes a in upper triangular form).

x_i = { b_i - sum from{j=i+1} to{j=n} a_ij x_j } over { a_ii} ~~~~~~ i=n-1,`n-2,`...,`1 HOW DO I CODE THIS!?

Starting index of 1:

xn = bn/ann	(Do this part outside the loop)

For Loop – Range = i = n-1 to 1 (stepping backward)
sum = get_sum(a,x,i)	This is a function call to get_sum
xi = ( bi – sum)/aii

function get_sum(a,x,i):
sum = 0	Initialize the sum
For Loop – Range j = i+1 to j = n
sum = sum + aij xj
return sum

Starting index of 0 (python):

xn-1 = bn-1/an-1,n-1	(Do this part outside the loop)

For Loop – Range = i = n-2 to 0 (stepping backward)
sum = get_sum(a,x,i)	This is a function call to get_sum
xi = ( bi – sum)/aii

function get_sum(a,x,i):
sum = 0	Initialize the sum
For Loop – Range j = i+1 to j = n-1
sum = sum + aij xj
return sum

Now with specific values here is what it would happen in code (not coded this way, but just to explain):

This assumes a starting index of 0, n = 4…

x3 = b3/a3,3	(Do this part outside the loop)

For Loop – Range = i = 2 to 0 (stepping backward)

i=2:
sum = get_sum(a,x,2)	This is a function call to get_sum
x2 = ( b2 – sum)/a22

function get_sum(a,x,2):
sum = 0	Initialize the sum
For Loop – Range j = 3 to j = 3

j = 3:
sum = 0 + a23 x3
return sum

i=1:
sum = get_sum(a,x,1)	This is a function call to get_sum
x1 = ( b1 – sum)/a11

function get_sum(a,x,1):
sum = 0	Initialize the sum
For Loop – Range j = 2 to j = 3

j = 2:
sum = 0 + a12 x2
j = 3:
sum = sum + a13 x3

return sum

i=0:
sum = get_sum(a,x,0)	This is a function call to get_sum
x0 = ( b0 – sum)/a00

function get_sum(a,x,0):
sum = 0	Initialize the sum
For Loop – Range j = 1 to j = 3

j = 1:
sum = 0 + a01 x1
j = 2:
sum = sum + a02 x2
j = 3:
sum = sum + a03 x3
return sum

Gauss Elimination Example (3x3 in augmented form):
Gauss = Forward elim. + Normalizing Pivots as we go + back substitution
stack{ x_1 - 3x_2 + x_3 = 4 # 2x_1 -8x_2 + 8x_3 = -2 # -6x_1 + 3x_2 -15x_3 = 9}

left[ {matrix { 1# -3# 1# 4## 2 # -8 # 8 # -2 ## -6 # 3 # -15 # 9 } } right]	stack { {-2R_1+R_2 rightarrow R_2^' } # { 6R_1 + R3 rightarrow R_3^' }} -2 ~ left[ {matrix { 1# -3# 1# 4} } right] newline left[ {matrix { -2# 6# -2# -8} } right] newline left[ {matrix { 2# -8# 8# -2} } right] newline left[ {matrix { 0# -2# 6# -10} } right] = R_2^{ ' } 6 ~ left[ {matrix { 1# -3# 1# 4} } right] newline left[ {matrix { 6# -18# 6# 24} } right] newline left[ {matrix { -6# 3# -15# 9} } right] newline left[ {matrix { 0# -15# -9# 33} } right] = R_3^{ ' }

left[ {matrix { 1# -3# 1# 4## 0 # -2 # 6 # -10 ## 0 # -15 # -9 # 33 } } right]	R_2^' over -2 rightarrow R_2^{ ''} left[ {matrix { 0# -2# 6# -10} } right] / -2 = left[ {matrix { 0# 1# -3# 5} } right] = R_2^{ ''}

left[ {matrix { 1# -3# 1# 4## 0 # 1 # -3 # 5 ## 0 # -15 # -9 # 33 } } right]	15 R_2^{ '' }+ R_3^' rightarrow R_3^{ '' } 15 ~ left[ {matrix { 0# 1# -3# 5} } right] newline left[ {matrix { 0# 15# -45# 75} } right] newline left[ {matrix { 0# -15# -9# 33} } right] newline left[ {matrix { 0# 0# -54# 108} } right] = R_3^{ '' }

left[ {matrix { 1# -3# 1# 4## 0 # 1 # -3 # 5 ## 0 # 0 # -54 # 108 } } right]	R_3^{ '' } over -54 rightarrow R_3^{ ''' } left[ {matrix { 0# 0# -54# 108} } right] / -54 = left[ {matrix { 0# 0# 1# -2} } right]

left[ {matrix { 1# -3# 1# 4## 0 # 1 # -3 # 5 ## 0 # 0 # 1 # -2 } } right]	stack { {(1) x_3 = -2 rightarrow x_3 = -2} # {(1)x_2 + (-3) (-2) = 5 rightarrow x_2 = -1}# {(1)x_1 + (-3)(-1) + (1)(-2) = 4 rightarrow x_1 = 3 }}

Generalize
We start with:
 left[ {matrix{a_11 # a_12 # a_13 #a_14 ## a_21 # a_22 # a_23# a_24 ## a_31 # a_32 # a_33# a_34 ## a_41 # a_42 #a_43 #a_44} }right] left[ {matrix{ x_1 ## x_2 ## x_3 ## x_4 } } right] = left[ {matrix{ b_1 ## b_2 ##b_3 ##b_4} } right] and we are trying to make it look like:

left[ {matrix{a_11 # a_12 # a_13 #a_14 ## 0 # a_22 '# a_23 '# a_24 '## 0 # 0# a_33 ''# a_34 '' ## 0 #0 #0 #a_44 '''} }right] left[ {matrix{ x_1 ## x_2 ## x_3 ## x_4 } } right] = left[ {matrix{ b_1 ## b_2 ##b_3 ##b_4} } right] where a22' has been modified from it's value.

The first equation is the pivot equation and a11 is the pivot coefficient. Here is how we can use it to operate on the other rows/equations to get the matrix in the upper triangular form. We also define m21 = a21/a11.

alignl{~~~~~~a_21 x_1 + a_22 x_2 + a_23 x_3 + a_24 x_4 = b_2} newline alignl{- m_21(a_11 x_1 + a_12 x_2 + a_13 x_3 + a_14 x_4 = b_1) }newline alignl{ ~~~~~~0 + ( a_22-m_21 a_12)x_2 + (a_23 - m_21 a_13) x_3 + ( a_24-m_21 a_14 ) x_4 = b_2 - m_21 b_1} newline alignl{ ~~~~~~a_22 ' x_2 + a_23 'x_3 + a_24 'x_4 = b_2 '}

The same operation is performed for each row (eliminating the first term in each equation/row.

Another example:

left[ {matrix{0.143 # 0.357 # 2.01## -1.31 # 0.911# 1.99## 11.2 # -4.30# -0.605} }right] left[ {matrix{ x_1 ## x_2 ## x_3 } } right] = left[ {matrix{ -5.173 ## -5.458 ##4.415 } } right]

Augmented form
It's helpful when actually implementing Gauss elimination to represent the problem as a single matrix in augmented form:

left[ {matrix{0.143 # 0.357 # 2.01 # -5.173## -1.31 # 0.911# 1.99 # -5.458## 11.2 # -4.30# -0.605 #4.415} }right]

Normalizing Pivots
One process that “helps” with this solution is to normalize the row that you are working on.. this means dividing the entire row by the pivot element. So for the first row as the pivot row:

left[ {matrix{1.00 # 2.50 # 14.1 # -36.2## -1.31 # 0.911# 1.99 # -5.46## 11.2 # -4.30# -0.605 #4.42} }right]

Note we have also rounded to three digits… we will keep this convention throughout this example (to make a point!).

Now you have to try to do the forward elimination on row 2:

left[ {matrix{1.00 # 2.50 # 14.1 # -36.2## 0.00 # 4.19# 20.5 # -52.9## 11.2 # -4.30# -0.605 #4.42} }right]

Now do forward elimination on row 3

left[ {matrix{1.00 # 2.50 # 14.1 # -36.2## 0.00 # 4.19# 20.5 # -52.9## 0.00 # -32.3# -159 #409} }right]

Now normalize the second row

left[ {matrix{1.00 # 2.50 # 14.1 # -36.2## 0.00 # 4.19# 20.5 # -52.9## 0.00 # -32.3# -159 #409} }right]

Now do elimination on the third row

left[ {matrix{1.00 # 2.50 # 14.1 # -36.2## 0.00 # 1.00# 4.89 # -12.6## 0.00 # 0.00# -1.00 #2.00} }right]

Now do normalize the third row

left[ {matrix{1.00 # 2.50 # 14.1 # -36.2## 0.00 # 1.00# 4.89 # -12.6## 0.00 # 0.00# 1.00 #-2.00} }right]

Show that x3 = -2.00, x2 = -2.82, x1 = -0.95

Also plug these values back into the original equations to see if they are correct??

Correct answers are x3 = -3, x2 = 2, x1 = 1 – Do you get the right answers!?

Rounding error was an issue! Of course it will be less of an issue on the computer where we can keep the numbers in double precision.

Also… there's another problem: There are large (2 orders of magnitude differences in the first column):

left[ {matrix{0.143 # 0.357 # 2.01 # -5.173## -1.31 # 0.911# 1.99 # -5.458## 11.2 # -4.30# -0.605 #4.415} }right] Note – 0.143, -1.31, 11.2…

left[ {matrix{1.00 # 2.50 # 14.1 # -36.2## 0.00 # 4.19# 20.5 # -52.9## 11.2 # -4.30# -0.605 #4.42} }right] Goes to: left[ {matrix{1.00 # 2.50 # 14.1 # -36.2## 0.00 # 4.19# 20.5 # -52.9## 0.00 # -32.3# -159 #409} }right]

The value -0.605 went to -159… a loss of three decimal places! We will fix this later with partial pivoting.

Now how to do the algorithm for Gauss?

This assumes a starting index of 0!
left[ {matrix{a_00 # a_01 # a_02 #b_0 ## a_10 # a_11 # a_12# b_1 ## a_20 # a_21 # a_22# b_2 } }right] This is what we will write our algorithm for

Assume we have matrix a (which is 3 x 3) in a. Assume we have an augmented form with the RHS vector augmented onto a called ab. Matrix ab will be 3 x 4.
Augment: We need a function called augment to make ab (the augmented matrix)

Note: we have already done this… python numpy made this easy.

augment(a,b)
initialize a new matrix ab
for i= 0 to 2
for j=0 to 3
if j < 3
abij = aij
else
abij = bi
return ab

Generalize it!
augment(a,b)
for i= 0 to n-1
for j=0 to n
if j < n
abij = aij
else
abij = bi
return ab

Normalize: We need a function normalize that divides the entire row by the pivot element – note for Gauss elimination this only needs to proceed from the index to the right within this row.

We will send in the entire ab matrix and the index of the row we need to normalize. For example purposes we will send in an index of 1. This means we will be “normalizing” by the value ab11 in row 2 (which has an index of 1!):

normalize(ab,1)
ab_new = ab	#just get a new version of the original
norm = a1,1
for j = 1 to 3
ab_new1,j = ab1,j / norm
return ab_new

Here is exactly what will happen above:
j = 1:	ab_new1,1 = ab1,1 / norm	(this should give us 1.00000...)
j = 2:	ab_new1,2 = ab1,2 / norm
j = 3:	ab_new1,3 = ab1,3 / norm
Generalize it!
normalize(ab,i)
ab_new = ab	#just get a new version of the original
norm = ai,i
for j = i to n
ab_newi,j = abi,j / norm
return ab_new

Forward Elimination: Let's say we are pivoting on ab0,0 that means we are trying to eliminate ab1,0 and ab2,0.
left[ {matrix{ab_00 # ab_01 # ab_02 #ab_03 ## ab_10 # ab_11 # ab_12# ab_13 ## ab_20 # ab_21 # ab_22# ab_23 } }right]

Assuming ab0,0 is normalized we need to do the following:

- ab_10 left[ {matrix{1.00 # ab_01 # ab_02 #ab_03} }right] + left[ {matrix{ab_10 # ab_11 # ab_12 #ab_13} }right] = {} newline left[ {matrix{0.00 # ab_11-ab_10 (ab_01) # ab_12-ab_10 (ab_02) #ab_13 - ab_10 (ab_03)} }right]

Here's the loop to do what is above (note this is to eliminate ab10)

for j = 1 to 3
ab1,j = ab1,j – ab1,0 (ab0,j)

j = 1:	ab1,1 = ab1,1 – ab1,0 (ab0,1)
j = 2:	ab1,2 = ab1,2 – ab1,0 (ab0,2)
j = 3:	ab1,3 = ab1,3 – ab1,0 (ab0,3)

Generalize it! – if the pivot row is i, the pivot element is abi,i and the element being eliminated is abi+1,i
for j = i+1 to n
abi+1,j = abi+1,j – abi+1,i (abi,j)	Compare to example above

 Note this only eliminates… to do this even more generally… have to work through all rows below i.

Also: In code we should go ahead and perform the operations above on element just below i,i…
The process above needs to be applied to every row below the pivot row, ab0,0 is the pivot

for k = 1 to 2
for j = 1 to 3
abk,j = abk,j – abk,0 (ab0,j)

k = 1:
j = 1:	ab1,1 = ab1,1 – ab1,0 (ab0,1)
j = 2:	ab1,2 = ab1,2 – ab1,0 (ab0,2)
j = 3:	ab1,3 = ab1,3 – ab1,0 (ab0,3)
k = 2:
j = 1:	ab2,1 = ab2,1 – ab2,0 (ab0,1)
j = 2:	ab2,2 = ab2,2 – ab2,0 (ab0,2)
j = 3:	ab2,3 = ab2,3 – ab2,0 (ab0,3)

Generalize it!

for k = i+1 to n-1
for j = i+1 to n
abk,j = abk,j – abk,i (abi,j)

We need to normalize after each pivot row and we need to use all rows as pivot rows except the last row… so

ab = augment(a,b)
for i = 0 to n-2
normalize(ab,i)
for k = i+1 to n-1
for j = i+1 to n
abk,j = abk,j – abk,i (abi,j)

Gauss Elimination with Partial Pivoting

Gauss Elimination works best when the pivot with the largest possible absolute value is chosen.

So the first pass we would identify the largest value in the first column, going back to the augmented form for a previous example:

left[ {matrix{0.143 # 0.357 # 2.01 # -5.173## -1.31 # 0.911# 1.99 # -5.458## 11.2 # -4.30# -0.605 #4.415} }right] → left[ {matrix{11.2 # -4.30# -0.605 #4.415 ## -1.31 # 0.911# 1.99 # -5.458##0.143 # 0.357 # 2.01 # -5.173 } }right]

Seems simple enough… we just swap rows. How would an algorithm need to work to do this?

(Assuming an starting index of zero)
left[ {matrix{ab_00 # ab_01 # ab_02 #ab_03 ## ab_10 # ab_11 # ab_12# ab_13 ## ab_20 # ab_21 # ab_22# ab_23 } }right]

index = 0 # We are going to place the best row first – keep track in index
initialize order vector – order[nx1]	order = [0,1,2]
max = abs(a0,0)
for i = 1 to 2 #examine all rows
if abs(ai,0) > max
index = i
max = abs(ai,0)
#now do a row swap
# index = 2
tmp = order[0]	#temporarily store original val. Of what was in row 0
# tmp = 0
order[0]= order[index]	#put new row 0 in correct place in order vector
# order[0] = order[2] = 2
order[index] = tmp	#complete row swap
# order[2] = 0
# order = [2,1,0]

Here are the actual values for the above matrix if we carried this out:

index = 0
order = [0, 1, 2]
max = abs(a0,0) (0.143)
for i = 1 to 2 #examine all rows
i = 1:
if abs(a1,0) (1.31) > max (0.143)
index = i (1)
max = abs(a1,0) (1.31)
i = 2:
if abs(a2,0) (11.2) > max (1.31)
index = i (2)
max = abs(a2,0) (11.2)

tmp = order[0] (0)
order[0]= index (2) #here's how we actually swap rows
order[2]= tmp (0)

# order vector will now look like: [2,1,0]
# so for the moment following would be true.…

aorder[0],0 = 11.2 while a0,0 is still 0.143

After this row exchange the matrix will look like:

left[ {matrix{ab_{order[0],0} # ab_{order[0],1} # ab_{order[0],2} #ab_{order[0],3} ## ab_{order[1],0} # ab_{order[1],1} # ab_{order[1],2}# ab_{order[1],3} ## ab_{order[2],0} # ab_{order[2],1} # ab_{order[2],2}# ab_{order[2],3} } }right] ← This is how we will deal with matrix in code

Which acheives :
left[ {matrix{0.143 # 0.357 # 2.01 # -5.173## -1.31 # 0.911# 1.99 # -5.458## 11.2 # -4.30# -0.605 #4.415} }right] → left[ {matrix{11.2 # -4.30# -0.605 #4.415##-1.31 # 0.911# 1.99 # -5.458 ## 0.143 # 0.357 # 2.01 # -5.173 } }right]

Note this process can process each time you move to a new pivot row… but you only need to proceed below the pivot.
Gauss-Jordan Elimination

left[ {matrix{a_11 # a_12 # a_13 #a_14 ## a_21 # a_22 # a_23# a_24 ## a_31 # a_32 # a_33# a_34 ## a_41 # a_42 #a_43 #a_44} }right] left[ {matrix{ x_1 ## x_2 ## x_3 ## x_4 } } right] = left[ {matrix{ b_1 ## b_2 ##b_3 ##b_4} } right] → left[ {matrix{1 # 0 # 0 #0 ## 0 # 1 # 0# 0 ## 0 # 0 # 1# 0 ## 0 # 0 #0 #1} }right] left[ {matrix{ x_1 ## x_2 ## x_3 ## x_4 } } right] = left[ {matrix{ b_1 ' ## b_2 ' ##b_3 '##b_4 '} } right]

So the solution will be contained in the b' vector.

In terms of an algorithm, this is very similar to Gauss elimination… we should include pivoting here, but note pivoting now would include all elements above and below the pivot. And now elimination is carried out above and below the pivot also.

First augment the matrix:
left[ {matrix{a_11 # a_12 # a_13 #a_14 # b_1 ## a_21 # a_22 # a_23# a_24 # b_2 ## a_31 # a_32 # a_33# a_34 # b_3 ## a_41 # a_42 #a_43 #a_44 # b_4} }right] → left[ {matrix{1 # 0 # 0 #0 # b_1 '## 0 # 1 # 0# 0 # b_2 '## 0 # 0 # 1# 0 # b_3 '## 0 # 0 #0 #1 # b_4 '} }right]

As you might guess… programming this is not too different than Gauss Elimination with Pivoting… the ranges of all the for loops change and there is additional logic required to not do operations on the pivot row itself.

LU Decomposition
It is possible to find [a]-1 the inverse of [a]. But it is a time consuming calculation with many operations required. More operations means more round-off error. If the inverse will be used many times… it is sometimes worth it, but even in these cases.. there is an alternative called LU Decomposition. Here is how it works:

[ L] = Lower Triangular
[ U ] = Upper Triangular

left[ {matrix{a_11 # a_12 # a_13 #a_14 ## a_21 # a_22 # a_23# a_24 ## a_31 # a_32 # a_33# a_34 ## a_41 # a_42 #a_43 #a_44 } }right] ~= ~ left[ {matrix{L_11 # 0 # 0 # 0 ## L_21 # L_22 # 0# 0 ## L_31 # L_32 # L_33# 0 ## L_41 # L_42 #L_43 #L_44} } right] ~~left[ {matrix{1 # U_12 # U_13 # U_14 ## 0 # 1 # U_23# U_24 ## 0 # 0 # 1# U_34 ## 0 # 0 #0 #1} } right]

This would be helpful for several reasons.

Define
[ U ][ x ]=[ y ] Equation 1

so that
[ L ][ y ]=[ b ] Equation 2
So the process is to:
1. Solve Eq. 2 for [y] (using forward elimination)
2. Solve Eq. 1 for [x] (using back substitution)

To be clear:

How do you get [L] and [U]? Please see the algorithm development for LU decomposition using Crout’s Method.

Of course we would only do this if we were going to solve this problem with the same [a] many times… this does come up in real problems… an example is below… if the reaction forces change only the RHS vector changes...

Matrix Inversion

There are two ways to get [a]-1 LU decomposition and Gauss-Jordan elimination. Please read your book for an example of how to use LU Decomposition. Here is how Gauss-Jordan would work:

left[ {matrix{a_11 # a_12 # a_13 #a_14 # 1#0#0#0 ## a_21 # a_22 # a_23# a_24 # 0# 1#0#0 ## a_31 # a_32 # a_33# a_34 # 0#0#1#0 ## a_41 # a_42 #a_43 #a_44 # 0#0#0#1} }right] → left[ {matrix{1#0#0#0 # a_11 '# a_12 '# a_13 '#a_14 '## 0# 1#0#0#a_21 '# a_22 '# a_23 '# a_24 ' ## 0#0#1#0 #a_31 '# a_32 '# a_33 '# a_34 ' ## 0#0#0#1#a_41 '# a_42 '#a_43 '#a_44 ' } }right]

So the a' matrix is the inverse. To do this one just needs to do forward and backward elimination and normalize the pivots. Once this is done you are left with an identity matrix where the a matrix was originally.

ITERATIVE METHODS

In these methods you write the unknown for each equation (row) in terms of all the other unknowns of the problem. For example:

a_11 x_1 + a_12 x_2 + a_13 x_3 + a_14 x_4 = b_1 newline a_21 x_1 + a_22 x_2 + a_23 x_3 + a_24 x_4 = b_2 → x_1 = [b_1 - ( a_12 x_2 + a_13 x_3 + a_14 x_4)]/ a_11 newline x_2 = [b_2 - ( a_21 x_2 + a_23 x_3 + a_24 x_4)]/ a_22

To get the process started you assume values for x1 – xn. The general form of the x equations above would be:

x_i = { 1} over { a_ii } left[ { b_i - sum from { j=1, j <> i } to { j=n} { a_ij x_j} } right]~~~~~~~~~i=1,2,...,n Equation 3

This technique when it works is very fast… all we really have to do is run equation 4 repeatedly. It is many fewer operations than the non-iterative techniques. It is almost like doing only the back substitution step in Gauss elimination. There is an issue… it will not always converge. It will converge when:

abs {a_ii} > sum from { j=1, j <> i } to { j=n} { abs{a_ij} }

This has to be true for each row… so one would typically reorder a matrix to make this as true as possible! In other words make it so that aii for each row is optimized to be as large as possible. This is called a diagonally dominant matrix.

Jacobi method
Let {x_i}^{ (2) } be the value of xi for the second iteration. It will be based on all of the x values from the first iteration {x_i}^{ (1) } . So using Eq. 4 above…
{x_i}^{(2)} = {1} over { a_ii }left[ { b_i - sum from { j=1, j <> i } to { j=n} { a_ij {x_j}^{(1)} } } right]~~~~~~~~~i=1,2,...,n

In general
{x_i}^{(k+1)} = {1} over { a_ii }left[ { b_i - sum from { j=1, j <> i } to { j=n} { a_ij {x_j}^{(k)} } } right]~~~~~~~~~i=1,2,...,n

The x values are iterated until the approximate relative fractional error is less than a stopping criterion, { %epsilon }_s

lline { { {x_i}^{(k+1) } } - {x_i}^{(k) } } over { {x_i}^{(k+1) } } rline < {%epsilon}_s
This must be true for all rows.

Note the updates for x-values all occur at the end of each iteration. Even though you actually have new values theoretically have new values {x_j}^{ (k+1) } for values of j less than i.

Gauss-Siedel
The only difference between Jacobi and Gauss-Siedel (GS) is that GS uses the best possible values for the x values… that means using the {x_j}^{ (k+1) } for values of j less than i. This converges faster than Jacobi… so this is very commonly used for many engineering problems. So for example:
{x_1}^{(k+1)} = {1} over { a_11 }left[ { b_1 - sum from { j=1, j <> i } to { j=n} { a_1j {x_j}^{(k)} } } right]

{x_i}^{(k+1)} = {1} over { a_ii }left[ { b_i - left( {sum from { j=1 } to { j=i-1} { a_ij {x_j}^{(k+1)} } + sum from { j=i+1 } to { j=n} { a_ij {x_j}^{(k)} } } right) } right]~~~~~~~~~i=1,2,...,n-1

{x_n}^{(k+1)} = {1} over { a_nn }left[ { b_1 - sum from { j=1 } to { j=n-1} { a_nj {x_j}^{(k+1)} } } right]

The x values are iterated until the approximate relative fractional error is less than a stopping criterion, { %epsilon }_s

lline { { {x_i}^{(k+1) } } - {x_i}^{(k) } } over { {x_i}^{(k+1) } } rline < {%epsilon}_s
This must be true for all rows.

Tridiagonal Systems
Sometimes (heat transfer, stress-strain, and other problems) the matrix to be solved is tridiagonal.

left[ {matrix{A_11 # A_12 # 0 #0#0 ## A_21 # A_22 # A_23# 0 # 0## 0 # A_32 # A_33# A_34#0 ## 0 # 0 #A_43 #A_44 #A_45 ## 0#0#0#A_54#A_55} }right]
Often these are more larger than 100x100… so there are a lot of zeros. We should not store those values or waste time using them in calculations. So there are algorithms to solve these problems. One such algorithm is the Thomas algorithm.

d_i = A_ii newline a_i = A_{ i,i+1 } newline b_i = A_{ i-1,i }

d= diagonal, a = above, b = below. The [d] vector has a length of n, while the [a] and [b] vectors are each of length n-1.
left[ {matrix{d_1 # a_1 # 0 #0#0 ## b_2 # d_2 # a_2# 0 # 0## 0 # b_3 # d_3# a_3#0 ## 0 # 0 #b_4 #d_4 #a_4 ## 0#0#0#b_5#d_5} }right]

As the book shows:

Basically you normalize each row as you proceed (starting at the second row) and then eliminate the below diagonal element, bi+1 just below the di. Then once the matrix is in the form above… use back substitution to get [x]. Note both the forward elimination and back substitution steps do not need to span the entire rows and columns… instead they are very quick calculations that only use the b, d, and a values.

ERROR, RESIDUAL, NORMS, CONDITION NUMBER

Error and Residual
For [a][x] = [b], if the true solution is [xTS], then the error in a numerical solution ([xNS]) is

[ e ]=[ x_TS ]-[ x_NS ]
Of course we don't know xTS, so… we can't directly calculate [e], but an estimate can be calculated.

Another way of assessing a solution is the residual, [r]

[ r ] = [b] - [b_NS] = [ a][ x_TS ]-[ a ][ x_NS ]

The residual measures the effect of the error in [xNS] on the right-hand-side vector [b].

Norms and Condition Numbers
It's easy to understand the scale of a scalar number using absolute values. The scale of a matrix is harder to assess and there are many ways to describe this. A norm is a way to do this. A norm must satisfy the following:

1. The norm is designated: ldline` [ a] `rdline and is positive and only equal to zero, if all the elements of the matrix are zero.
2. If you scale a matrix up by multiplying it by a scalar number, a, the norm should also scale up by a: ldline` %alpha[ a]` rdline = abs{ %alpha }` ldline` [ a]` rdline .
3. ldline` [ a][x ] `rdline <= ldline` [ a] `rdline `ldline` [ x] `rdline
4. ldline ` [ a+b] ` rdline <= ldline ` [ a] ` rdline + ldline ` [ b] ` rdline triangle inequality

All norms should follow the rules above.

Vector Norms

For a vector [v].

Infinity Norm
Equal to the largest magnitude component of [v].
ldline ` v `rdline _infinity = max abs { v_i } ~~~~ i = 1,2,3,...n

1-norm
The sum of the absolute values of the vector elements.
ldline ` v ` rdline _1 = sum from i = 1 to n abs{ v_i }

Euclidean 2-Norm
Square root of the sum of the squares of the vector elements
ldline ` v ` rdline _2 = left ( sum from i = 1 to n {v_i}^2 right ) ^{ 1/2}

Example vector: left[ {matrix{0.2#-5#3#0.4#0} }right]
ldline ` v `rdline _infinity = 5

ldline ` v ` rdline _1 = sum from i = 1 to n abs{ v_i } = 0.2+5+3+0.4+0=8.6

ldline ` v ` rdline _2 = left ( sum from i = 1 to n {v_i}^2 right ) ^{ 1/2} = ( 0.2^2+5^2+3^2+0.4^2+0^2 )^{1/2} = ( 34.2 )^{ 1/2 } = 5.8

Matrix Norms

For a matrix [a].

Infinity Norm
Equal to the largest value of summing up the magnitudes of each row of [a].
ldline ` a `rdline _infinity = max sum from j=1 to n abs { a_ij } ~~~~ i = 1,2,3,...n

1-norm
Equal to the largest value of summing up the magnitudes of each column of [a].
ldline ` a ` rdline _1 = max left[ {sum from i = 1 to n abs{ a_ij }} right]~~~~~j=1,2,...n

2-norm (spectral norm)
ldline ` a ` rdline _2 = max left ( {ldline` a v `rdline} over {ldline`v`rdline} right )
Note [v] is the vector corresponding to the eigenvalue of the matrix, l. Note there are muliple eigenvalues. We will talk more about this in the next chapter.

Euclidean Norm
Square root of the sum of the squares of the matrix elements (note does not need to be square…) matrix that is m x n.
ldline ` a ` rdline _{Euclidean} = left ( sum from i = 1 to m sum from j = 1 to n {a_ij}^2 right ) ^{ 1/2}

Example Matrix:

[a] = left[ {matrix{0.2#-5#3#0.4#0 ## -0.5 # 1 # 7 # -2 # 0.3 ## 0.6 #2 #-4 #3 #0.1 ## 3 #0.8# 2# -0.4# 3 ## 0.5 #3 #2 #0.4# 1} }right]

ldline ` a `rdline _infinity = max sum from j=1 to n abs { a_ij } ~~~~ i = 0.5+1+7+2+0.3 = 10.8

ldline ` a ` rdline _1 = max left[ {sum from i = 1 to n abs{ a_ij }} right] = 3 + 7 + 4+2+2 = 18

ldline ` a ` rdline _{Euclidean} = left ( sum from i = 1 to m sum from j = 1 to n {a_ij}^2 right ) ^{ 1/2} = 0.2^2+5^2+3^2+0.4^2+.5^2+1^2+7^2+2^2+0.3^2+0.6^2+2^2+4^2+3^2 newline +0.1^2+3^2+0.8^2+2^2+0.4^2+3^2+0.5^2+3^2+2^2+0.4^2+1^2

Relationship of norms to error and residuals (be patient… big conclusion at the end!!)

[ r ] = [b] - [b_NS] = [ a][ x_TS ]-[ a ][ x_NS ] = [ a] ( `[ x_TS ]-[ x_NS ]`) = [ a][e ]

Which means if [a] is invertible

[ e] = [a ]^{ -1 }`[ r]

Recalling the property of norms: ldline` [ a][x ] `rdline <= ldline` [ a] `rdline `ldline` [ x] `rdline

­
ldline `[ e] `rdline = ldline`[a ]^{ -1 }`[ r]`rdline <= ldline`[a ]^{ -1 }`rdline `ldline`[ r]`rdline Equation 4

Also

ldline `[ r] `rdline = ldline`[a ]`[ e]`rdline <= ldline`[a ]`rdline `ldline`[ e]`rdline or
{ldline `[ r] `rdline} over {ldline`[a ]`rdline} <= ldline`[ e]`rdline Equation 5

If Eqs. 5-6 are combined:

{ldline `[ r] `rdline} over {ldline`[a ]`rdline} <= ldline`[a ]^{ -1 }`rdline `ldline`[ r]`rdline Equation 6

Now define the relative error as {ldline `[ e] `rdline} over {ldline` [x_TS]`rdline } and the relative residual as {ldline `[ r] `rdline} over {ldline` [b]`rdline }

Note the error, [e], cannot actually be calculated, but the residual can be calculated

[ r ] = [ a][ x_TS ]-[ a ][ x_NS ] =[b] - [ a ][ x_NS ]

Using the value of [r], one can put bounds on the relative error as follows, from Eqs. 6-7

{1} over {ldline`[x_TS ]`rdline}{ldline`[b ]`rdline} over {ldline`[b ]`rdline} {ldline `[ r] `rdline} over {ldline`[a ]`rdline} <= {ldline`[e ]`rdline} over { `ldline`[ x_TS]`rdline} <= {ldline`[a ]^{ -1 }`rdline `ldline`[ r]`rdline} over {ldline`[x_TS ]`rdline} {ldline`[b ]`rdline} over {ldline`[b ]`rdline} Equation 7

Rearrange to get:

{1} over {ldline`[a ]`rdline}{ldline`[b ]`rdline} over {ldline`[x_TS ]`rdline} {ldline `[ r] `rdline} over {ldline`[b ]`rdline} <= {ldline`[e ]`rdline} over { `ldline`[ x_TS]`rdline} <= ldline`[a ]^{ -1 }`rdline {ldline`[b ]`rdline} over {ldline`[x_TS ]`rdline} {ldline `[ r] `rdline} over {ldline`[b ]`rdline} Equation 8

Again use the fact that: ldline` [ a][x ] `rdline <= ldline` [ a] `rdline `ldline` [ x] `rdline Which means that

 ldline` [ a][x_TS ] `rdline = ldline` [ b ] `rdline <= ldline` [ a] `rdline `ldline` [ x_TS] `rdline or that {ldline` [ b ] `rdline } over {ldline` [ a] `rdline `ldline` [ x_TS] `rdline} <= 1

Also

ldline` [ x_TS ] `rdline = ldline` [ a ]^-1 [b] `rdline <= ldline` [ a]^-1 `rdline `ldline` [ b] `rdline or that {ldline` [ a ]^-1 `rdline ldline` [ b] `rdline} over {ldline` [ x_TS] `rdline }>= 1

The conclusion from above is that:

{ldline` [ b ] `rdline } over { `ldline` [ x_TS] `rdline} <= ldline` [ a] `rdline and that {ldline` [ b ] `rdline } over { `ldline` [ x_TS] `rdline} >= 1 over {ldline` [ a]^-1 `rdline}

So if we were to substitute ldline` [ a] `rdline for in the RHS of Eq. 9… because this would only make the inequality more true.

And if we were to substitute 1 over {ldline` [ a]^-1 `rdline} for {ldline` [ b ] `rdline } over { `ldline` [ x_TS] `rdline} in the LHS of Eq. 9… this would only make the inequality more true.

So finally: {1} over {ldline`[a ]`rdline ldline`[a ]^-1`rdline} {ldline `[ r] `rdline} over {ldline`[b ]`rdline} <= {ldline`[e ]`rdline} over { `ldline`[ x_TS]`rdline} <= ldline`[a ]^{ -1 }`rdline ldline`[a ]`rdline {ldline `[ r] `rdline} over {ldline`[b ]`rdline} THIS IS THE BIG CONCLUSION!

Why is this important… LHS = lower bound on relative error and the RHS = upper bound on error!

So if you multiply {1} over {ldline`[a ]`rdline ldline`[a ]^-1`rdline} by the relative error, {ldline `[ r] `rdline} over {ldline`[b ]`rdline} , you get the lowest possible relative error, {ldline`[e ]`rdline} over { `ldline`[ x_TS]`rdline} .

If you mutiply {ldline`[a ]`rdline ldline`[a ]^-1`rdline} by the relative error, {ldline `[ r] `rdline} over {ldline`[b ]`rdline} , you get the largest possible relative error, {ldline`[e ]`rdline} over { `ldline`[ x_TS]`rdline} .

This combination of {ldline`[a ]`rdline ldline`[a ]^-1`rdline} is hence very important in knowing what kind of error to expect in solving a linear algebra problem.

This known as the condition number.

Cond[a] = ldline`[a ]`rdline ldline`[a ]^-1`rdline

- Cond[I] = 1 Cond of all other matrices > 1
- When Cond is close to 1,
  - {1} over {Cond[a]} {ldline `[ r] `rdline} over {ldline`[b ]`rdline} <= {ldline`[e ]`rdline} over { `ldline`[ x_TS]`rdline} <= Cond[a]{ldline `[ r] `rdline} over {ldline`[b ]`rdline}
  - The relative error bounds are close to one another… and the relative error is of the same order of magnitude (factor of 10) as the relative residual.
- If Cond[a] is much larger than 1, then … the precision of the solution will be very limited (relative error bounds are very large).

[a] = left[ {matrix{0.2#-5#3#0.4#0 ## -0.5 # 1 # 7 # -2 # 0.3 ## 0.6 #2 #-4 #3 #0.1 ## 3 #0.8# 2# -0.4# 3 ## 0.5 #3 #2 #0.4# 1} }right] [a]^-1 = left[ {matrix{-0.7079#2.5314#2.4312#0.9666#-3.9023 ## -0.1934 # 0.3101 # 0.2795 # 0.0577 # -0.2941 ## 0.0217 #0.3655 #0.2861 #0.0506 #-0.2899 ## 0.2734 #-0.1299# 0.1316# -0.1410# 0.4489 ## 0.7815 #-2.8751 #-2.6789 #-0.7011# 4.2338} }right]

Find Cond[a] using the infinity norm.